## Slide 1: Section III: Non-smooth Newton Methods

## Slide 2: Non-smooth Newton Methods
Notes: I will start by refreshing my memory of how a Newton method works for solving a root search problem.
CLICK 1
I want to find the root of some vector function F, I am given some initial value x that is not a root, and is now looking for the solution x star which is a root.
CLICK 2
My first step is to do a first order Taylor approximation around the initial x value
CLICK 3
From this approximation called the Newton equation I can solve for delta x also called the search direction or Newton direction. Once I have delta x I can use it to update the initial x value and obtain x star. This step of adding the search direction to the current value is called the Newton update. The updated value will not be the perfect root I am looking for as there is some hopefully small error coming from the Taylor approximation. So, I often need to repeat this process until my updated iterate is close enough to be a root. Sometimes the search direction is multiplied by a step length to improve on the convergence of this numerical method. I will ignore this here and instead just focus on the raw building blocks that I need to build a Newton method. I need a F function and I need to be able to compute the derivative of F with respect to x. This is called the Jacobian of F.

## Slide 3: Non-smooth Newton Methods
Notes: I will now start to find out how to reformulate a linear complementarity problem into a root search problem.
CLICK 1
I am given the linear complementarity problem like this
CLICK 2
I want to find a F function like this. To do so I will make use of nonlinear complementarity problem functions. These are also just called ncp functions for short.
CLICK 3
They are defined by any function where the roots are equivalent to the complementarity condition. There exist many different functions of this type. I have already shown how the minimum map is one such function. Here I just use the symbol psi to denote any such choice. If I have a ncp function, then I can now define the root search problem as follows
CLICK 4
So far everything appear very easy and straightforward. However, we need to consider how to compute the derivative of the ncp functions. Remember the minimum map function is nonsmooth. So, the derivative do not exist in the classical sense. Luckily, we can work with a generalization of the concept. I will show this by example.

## Slide 4: Non-smooth Newton Methods
Notes: The Fischer-Burmeister function is one such ncp function and it is defined like this
CLICK 1
The Fischer-Burmeister function is interesting because, unlike the minimum-map, it is smooth everywhere apart from the point where and b both are zero.
CLICK 2
This is can be seen easily if we plot the Fischer Burmesiter function. Observe the cusp at the origin
CLICK 3
I can now create my F-function by using the Fischer-Burmesiter function. The only headache I have is to figure out how to compute the Jacobian of this Fischer-Burmester root search function that I get.

## Slide 5: Non-smooth Newton Methods
Notes: I will start with getting the derivatives of the Fischer Burmeister function at points where the function is smooth.
CLICK 1
This means the point a comma b is nonzero. Now I can take the smooth derivative by applying calculus
CLICK 2
I will define these two extra helper functions that I call alpha and beta to mean the derivative with respect to a and b respectively. This is just convenient later on when I have to write up longer expressions.
For now, I have ignored the singe non-smooth point of the Fischer Burmeister function. Clearly, we can see that alpha and beta becomes undefined if both a and b are equal to zero.
According to theory any element in Clarke’s generalized Jacobian which is defined as the convex hull of the B sub-differential will work for us to get a Newton method that converge. There are infinite many choices in the generalized Jacobian, so we just arbitrarily pick one element that is nice looking.
CLICK 3
This means alpha is zero and beta is minus one when a and b are both zero.

## Slide 6: Non-smooth Newton Methods
Notes: I used the Fischer Burmeister function to reformulate the linear complementarity problem into the nonsmooth root search problem
CLICK 1
I now apply the chain rule to the i-th component of F to find the derivative with respect to x j.
CLICK 2
Observe that I get the partial derivatives of x i and y i with respect to x j multiplied by the alpha and beta terms.
CLICK 3
The first partial derivative term
CLICK 4
is trivially to compute
CLICK 5
for the second term
CLICK 6
I need to remember that y is equal to A times x plus B.
CLICK 7
The notation is not very compact so I will define the two diagonal matrices holding alpha and beta terms.
CLICK 8
Using these
CLICK 9
I can finally write up the Jacobian that I need for the Newton method in a quite elegant way like this.

## Slide 7: Non-smooth Newton Methods
Notes: I have now shown how the linear complementarity problem can be solved with a Fischer Burmeister Newton method. I will now take it one step further and show how to apply the Newton method for a nonlinear complementarity problem model of the contact problem.
So, I need to show how we can put the nonlinear contact model into a NCP function. I will just go with the Fischer Burmeister function to be specific, but in principle the techniques I cover will work for any type of NCP function.
CLICK 1
I will start with the position level non-penetration constraints. Here phi is the gap function, q is the generalized positions and lambda n is the normal force. This complementarity condition is reformulated to the root search problem
CLICK 2
Shown here. For the Newton method I need to know the derivatives
CLICK 3
They are fortunately easily computed like this.
Many simulators uses a velocity level non-penetration constraint. So, I will also just quickly show how to work this. It looks like this
CLICK 4
Here v_n is the relative velocity in the normal direction at the point of contact. The reformulation follows like this
CLICK 5
Finally, the derivates are given by this
CLICK 6
The contact space velocity is a linear function of the generalized velocities given by the u vector here. This means I am interested in the partial derivative with respected to generalized velocities and not position.
CLICK 7
The partial derivative of the contact space velocity v_n with respect to the generalized velocities u is simply the Jacobian as seen from the kinematic relationship. I can substitute in the contact Jacobian in place of the partial derivative when computing the value of the partial derivatives.
Next, I will move on to how we can incorporate friction.

## Slide 8: Non-smooth Newton Methods
Notes: Now let us investigate how to model friction. I will start from the principle of maximum dissipation.
CLICK 1
Here v_t is the relative tangential velocity at the point of contact and lambda t is the friction force and mu is the coefficient of friction.
Using method of lagrange multipliers I can write up the Lagrangian for this minimization problem
CLICK 2
Here gamma is the lagrange multiplier. The first order optimality conditions for this minimization problem can now be described by this set of equations.
CLICK 3
I use the symbol s for the gradient of the Lagrangian. Observe how gamma now controls stick and slip behavior. The first order optimality conditions is a complementarity condition and this I use to reformulate the friction problem
CLICK 4
Now I have a root-search reformulation of the friction model given by the equation for the gradient equal to zero and the equation with the Fischer Burmeister function.
CLICK 5
Shown here in red boxes.
I now have reformulations for both normal and friction forces and all I am missing to do is to put it all together with the Newton Euler equations. I will do this next.

## Slide 9: Non-smooth Newton Methods
Notes: To put everything together I simply stack all the equations I have on top of each other like this
CLICK 1
Observe the first row is simply the Newton Euler equations. The newton iterate vector given by x contrains both generalized velocities, normal and friction forces and lagrange multipliers. The written notation can be a little verbose so I will just ease up the notation clutter by using these two shorthand notations
CLICK 2
With those in place it is not very hard to write up the Newton equation
CLICK 3
It looks like this. I notice that even though the Jacobian matrix of F looks a little scarry with all those partial derivatives inside of it. Each partial derivative is pretty straightforward to evaluate as I have shown in previous slides. This means I can now assemble and solve for my Newton direction.
The outline I used here, just used notation for a single contact point. However, it is not hard to extend the system by stacking multiple contacts together into one sub-block. The overall structure stays the same.